## Slide 1
Royal Meteorological Institute of Belgium
1
Royal Observatory of Belgium
2
Belgian Institute for Space Aeronomy
3
Max Planck Institute for Chemistry
4
Solar-Terrestrial Centre of Excellence
5
Assessment of IGS repro1 IWV trends by comparison with ERA-interim and GOMESCIA satellite data
R. Van Malderen1,5, E. Pottiaux2,5, H. Brenot3,5, S. Beirle4, T. Wagner 4, H. De Backer1, and C. Bruyninx2,5
GNSS4SWEC-WG3 workshop, Thessaloniki, 11-13/05/2015

## Slide 2
Introduction: inter-technique comparison
Sensitivity analysis of meteorological variables
IWV trends and correlations
Conclusions and perspectives
Outline
ROB
GNSS4SWEC workshop
Thessaloniki, Greece 11-13 May 2015

## Slide 3
GNSS4SWEC workshop
Thessaloniki, Greece 11-13 May 2015
IWV techniques intercomparison at 28 sites world-wide (NH)
IGS CIMEL radiosondes GOMESCIA AIRS
ROB
Van Malderen, R., Brenot, H., Pottiaux, E., Beirle, S., Hermans, C., De Mazière, M., Wagner, T., De Backer, H., and Bruyninx, C.: A multi-site intercomparison of integrated water vapour observations for climate change analysis, Atmos. Meas. Tech., 7, 2487-2512, doi:10.5194/amt-7-2487-2014, 2014.
Sensitivity analysis
Conclusions & perspectives
Introduction
IWV trends & correlations

## Slide 4
IGS stations selected (homogenous processing for data since 1995 to 2011)
ROB
GNSS4SWEC workshop
Thessaloniki, Greece 11-13 May 2015
Sensitivity analysis
Conclusions & perspectives
Introduction
IWV trends & correlations

## Slide 5
ROB
Tm
water-vapour-weighted atmospheric mean temperature
NWP models (reanalyses)
NCEPNCAR (I+II)
ERA-interim
Tm = 70.2 + 0.72Ts
Bevis et al. 1992
Zenith Total Delay (ZTD)
Ts
ps
Integrated water vapour (IWV)
synop stations
reanalyses
 sensitivity analysis of ps, Tm, Ts , and data sources by isolating the  influence of a given parameter/dataset
GNSS4SWEC workshop
Thessaloniki, Greece 11-13 May 2015
Conclusions & perspectives
IWV trends & correlations
Introduction
Sensitivity analysis

## Slide 6
ROB
 | bias (mm) | abs bias (mm) | SD | R² | trend (mm/dec) | abs trend (mm/dec)
[a] | Tm ERA: influence IGS data |  |  |  |  | 
IWV ERA | -0.313±1.011 | 0.669±0.818 | 3.807 | 0.962 | -0.102±0.457 | 0.322±0.338
[b] | Tm ERA: influence Ps |  |  |  |  | 
TmERA P synop* | -0.200±0.614 0.031±0.611 | 0.301±0.570 0.357±0.494 | 7.575 0.786 | 0.961 0.989 | -0.290±0.752 0.052±0.401 | 0.353±0.724 0.277±0.292
[c] | T ERA P synop: influence Ts |  |  |  |  | 
TP synop* | 0.009±0.025 0.267±0.622 | 0.020±0.017 0.503±0.447 | 0.029 2.878 | 1.000 0.979 | 0.013±0.244 -0.197±0.879 | 0.107±0.219 0.502±0.744
[d] | Tm ERA: influence Bevis et al. regression |  |  |  |  | 
TP ERA | 0.044±0.092 0.508±1.583 | 0.069±0.075 1.235±1.108 | 0.025 8.099 | 1.000 0.804 | -0.004±0.031 -0.101±0.213 | 0.018±0.025 0.188±0.140
[e] | Tm ERA P synop: influence Ts and Bevis et al. regression |  |  |  |  | 
TP synop* | 0.026±0.071 | 0.051±0.055 | 0.052 | 1.000 | 0.001±0.248 | 0.110±0.221
[f] | Tm ERA: influence reanalysis dataset |  |  |  |  | 
Tm NCEP | -0.034±0.286 | 0.168±0.233 | 0.154 | 0.995 | -0.015±0.144 | 0.083±0.118
[g] | Tm ERA: observational vs. reanalysis dataset |  |  |  |  | 
TP synop* | -0.073±0.403 | 0.223±0.342 | 4.705 | 0.971 | -0.210±0.667 | 0.259±0.649
Conclusions & perspectives
IWV trends & correlations
Introduction
Sensitivity analysis

## Slide 7
ROB
IGS, Tm ERAinterim
IWV trends [mm/dec] 1997-Mar 2011
Conclusions & perspectives
Introduction
Sensitivity analysis
IWV trends & correlations

## Slide 8
ROB
ERAinterim
IWV trends [mm/dec] 1997-Mar 2011
Conclusions & perspectives
Introduction
Sensitivity analysis
IWV trends & correlations

## Slide 9
ROB
GOMESCIA
IWV trends [mm/dec] 1997-Mar 2011
Conclusions & perspectives
Introduction
Sensitivity analysis
IWV trends & correlations

## Slide 10
ROB
IGS, Tm ERAinterim
IWV trends [mm/dec] 1997-Mar 2011
Conclusions & perspectives
Introduction
Sensitivity analysis
IWV trends & correlations

## Slide 11
ROB
Trend examples
large differences in IWV trends between the data sources at a given site
site dependent!
homogeneity of the IWV data sources!?!
GNSS4SWEC workshop
Thessaloniki, Greece 11-13 May 2015
Conclusions & perspectives
Introduction
Sensitivity analysis
IWV trends & correlations

## Slide 12
ROB
Homogeneity check
We calculated the “change points” of IWV differences of all stations of
  IGS_TmERAinterim – ERAinterim
  IGS_TmNCEPNCAR – NCEPNCAR
  IGS_TmERAinterim – NCEPNCAR
  IGS_TmNCEPNCAR – ERAinterim
… point-by-point and for monthly means @0h, 12h, 0h+12h
… by three different statistical tests (Pettitt-Mann-Whitney, Mann-Whitney-Wilcoxon, … Cumulative Sum technique*)
GNSS4SWEC workshop
Thessaloniki, Greece 11-13 May 2015
to be extended to GOMESCIA dataset
results are to be interpreted (identified change points should be linked to known changes in instrument, reanalysis changes)
we are open to compare/collaborate with other groups working on this, considering to host a GNSS4SWEC thematic sub-WG meeting @ Brussels!
Conclusions & perspectives
Introduction
Sensitivity analysis
IWV trends & correlations
*described in e.g. Van Malderen & De Backer, JGR, 2010

## Slide 13
ROB
Trend correlations: between data sources
GNSS4SWEC workshop
Thessaloniki, Greece 11-13 May 2015
fair agreement between IGS and ERAinterim IWV trends
poorer agreement between IGS and GOMESCIA trends (stronger moistening in GOMESCIA): differences in observation times? Impact of weather observation bias (partly clear sky) of GOMESCIA? Data homogeneity issues?
Conclusions & perspectives
Introduction
Sensitivity analysis
IWV trends & correlations

## Slide 14
ROB
Trend correlations: between 0h and 12h
GNSS4SWEC workshop
Thessaloniki, Greece 11-13 May 2015
very good agreement between IWV ERAinterim trends at 0h and 12h
a handful of IGS sites show unrealistic trends at 0h. Some additional filtering is needed here, to remove e.g. the ZTD day boundary jumps ( IGS repro 2!)
Conclusions & perspectives
Introduction
Sensitivity analysis
IWV trends & correlations
IGS
ERA-interim

## Slide 15
ROB
Trend correlations: between Ts and IWV
GNSS4SWEC workshop
Thessaloniki, Greece 11-13 May 2015
A physical law (the Clausius-Clapeyron equation) tells us that the water holding capacity of the atmosphere goes up at about 7% per degree Celsius/Kelvin increase in temperature
This is not well established by our datasets, in particular for GOMESCIA!
Conclusions & perspectives
Introduction
Sensitivity analysis
IWV trends & correlations
ERA-interim
GOMESCIA
IGS

## Slide 16
GPS IWV trends are not too strongly affected by the used meteorological dataset
 the trends are really in the Zenith Total Delay data
 the surface pressure has the largest impact
Data screening (especially the 0h data at some stations) and homogenisation should be further developed.
The IWV trends based on the IGS ZTDs agree fairly well with model reanalysis trends, stronger deviations with completely independent GOMESCIA trends.
What is the impact of the cloud cover on the GOMESCIA trends?
Link between IWV trends and temperature trends as function of geographical location, altitude, etc.
GPS IWV trends are not too strongly affected by the used meteorological dataset
 the trends are really in the Zenith Total Delay data
 the surface pressure has the largest impact
Data screening (especially the 0h data at some stations) and homogenisation should be further developed.
The IWV trends based on the IGS ZTDs agree fairly well with model reanalysis trends, stronger deviations with completely independent GOMESCIA trends.
What is the impact of the cloud cover on the GOMESCIA trends?
Link between IWV trends and temperature trends as function of geographical location, altitude, etc.
ROB
Introduction
Sensitivity analysis
IWV trends & correlations
Conclusions & perspectives
GNSS4SWEC workshop
Thessaloniki, Greece 11-13 May 2015

## Slide 17
Thank you!
painting by Jess Sutton
GNSS4SWEC workshop
Thessaloniki, Greece 11-13 May 2015